## Slide 1
Chapter 1 – Introduction

## Slide 2: Chapter 1 – Introduction
1.1 Electronic Design Automation (EDA)
1.2 VLSI Design Flow
1.3 VLSI Design Styles
1.4 Layout Layers and Design Rules
1.5 Physical Design Optimizations
1.6 Algorithms and Complexity
1.7 Graph Theory Terminology
1.8 Common EDA Terminology

## Slide 3: 1.1 Electronic Design Automation (EDA)
Moore’s Law
In 1965, Gordon Moore (Fairchild) stated that the number of transistors on an IC would double every year. 10 years later, he revised his statement, asserting that they double every 18 months. Since then, this “rule” has been famously known as Moore’s Law.
Moore: „Cramming more components onto integrated circuits"
Electronics, Vol. 38, No. 8, 1965

## Slide 4: 1.1 Electronic Design Automation (EDA)
Impact of EDA technologies on overall IC design productivity and IC design cost

## Slide 5: 1.1 Electronic Design Automation (EDA)
Design for Manufacturability (DFM), optical proximity correction (OPC), and other techniques emerge at the design-manufacturing interface. Increased reusability of blocks, including intellectual property (IP) blocks.
2000 - now
First over-the-cell routing, first 3D and multilayer placement and routing techniques developed. Automated circuit synthesis and routability-oriented design become dominant. Start of parallelizing workloads. Emergence of physical synthesis.
1990 -2000
First performance-driven tools and parallel optimization algorithms for layout; better understanding of underlying theory (graph theory, solution complexity, etc.).
1985 -1990
More advanced tools for ICs and PCBs, with more sophisticated algorithms.
1975 -1985
Layout editors, e.g., place and route tools, first developed for printed circuit boards.
1965 -1975
Manual design only.
1950 -1965
Circuit and Physical Design Process Advancements
Time Period
© 2022 Springer Verlag

## Slide 6: 1.2 VLSI Design Flow
ENTITY test is port a: in bit; end ENTITY test;
DRC LVS
ERC
Circuit Design
Functional Design and Logic Design
Physical Design
Physical Verification and Signoff
Fabrication
System Specification
Architectural Design
Chip
Packaging and Testing
Chip Planning
Placement
Signal Routing
Partitioning
Timing Closure
Clock Tree Synthesis
© 2022 Springer Verlag

## Slide 7: 1.3 VLSI Design Styles
Layer Palette
Mouse Buttons Bar
Layout Windows
Drawing Tools
Cell Browser
Status Bar
Toolbar
Menu Bar
Text Windows
Layout editor
Locator

## Slide 8: 1.3 VLSI Design Styles
Common digital cells
 | IN | OUT
 | 0 | 1
 | 1 | 0
 | 1 | 0
 | 1 | 1
OR
INV
NOR
NAND
AND
IN1 | IN2 | OUT
0 | 0 | 0
1 | 0 | 0
0 | 1 | 0
1 | 1 | 1
IN1 | IN2 | OUT
0 | 0 | 0
1 | 0 | 1
0 | 1 | 1
1 | 1 | 1
IN1 | IN2 | OUT
0 | 0 | 1
1 | 0 | 0
0 | 1 | 0
1 | 1 | 0
IN1 | IN2 | OUT
0 | 0 | 1
1 | 0 | 1
0 | 1 | 1
1 | 1 | 0

## Slide 9: 1.3 VLSI Design Styles
Vdd
GND
OUT
IN2
IN1
OUT
IN2
IN1
OUT
IN1
Vdd
GND
IN2
Contact
Diffusion layer
p-type transistor
n-type transistor
Metal layer
Poly layer

## Slide 10: 1.3 VLSI Design Styles
Power (Vdd)-Rail
Ground (GND)-Rail
Contact
Vdd
GND
OUT
IN2
IN1
OUT
IN2
IN1
OUT
IN1
Vdd
GND
IN2
Diffusion layer
p-type transistor
n-type transistor
Metal layer
Poly layer
© 2022 Springer Verlag

## Slide 11: 1.3 VLSI Design Styles
Standard cell layout with a feedthrough cell
A
GND
Feedthrough Cell
Pad
Ground Pad
Routing Channel
Standard Cells
Power Pad
GND
Pad
Ground Pad
Standard Cells
Power Pad
A’
A
A’
VDD
VDD
Standard cell layout using over-the-cell (OTC routing
© 2022 Springer Verlag

## Slide 12: 1.3 VLSI Design Styles
Layout with macro cells
Pad
GND
PLA
RAM
Standard Cell Block
RAM
PLA
Routing Regions
VDD
© 2022 Springer Verlag

## Slide 13: 1.3 VLSI Design Styles
Field-programmable gate array (FPGA)
LB
LB
LB
SB
SB
LB
LB
LB
SB
SB
LB
LB
LB
LB
LB
LB
SB
SB
LB
LB
LB
SB
SB
LB
LB
LB
LB
LB
SB
SB
LB
LB
LB
SB
SB
LB
LB
LB
Logic Element
Switchbox
LB
Connection
© 2022 Springer Verlag

## Slide 14: 1.4 Layout Layers and Design Rules
Layout layers of an inverter cell with external connections
Contact
Metal1
polysilicon
p/n diffusion
Vdd
GND
Via
Metal2
Inverter Cell
External Connections
© 2022 Springer Verlag

## Slide 15: 1.4 Layout Layers and Design Rules
Size rules, such as minimum width: The dimensions of any component (shape), e.g., length of a boundary edge or area of the shape, cannot be smaller than given minimum values. These values vary across different metal layers.
Separation rules, such as minimum separation: Two shapes, either on the same layer or on adjacent layers, must be a minimum (rectilinear or Euclidean diagonal) distance apart.
Overlap rules, such as minimum overlap: Two connected shapes on adjacent layers must have a certain amount of overlap due to inaccuracy of mask alignment to previously-made patterns on the wafer.
Categories of design rules

## Slide 16: 1.4 Layout Layers and Design Rules
Categories of design rules
Minimum Width: a Minimum Separation: b, c, d
Minimum Overlap: e
a
d
c

b
e
: smallest meaningful technology-dependent unit of length
© 2022 Springer Verlag

## Slide 17: 1.5 Physical Design Optimizations
Technology constraints enable fabrication for a specific technology node and are derived from technology restrictions. Examples include minimum layout widths and spacing values between layout shapes.
Electrical constraints ensure the desired electrical behavior of the design. Examples include meeting maximum timing constraints for signal delay and staying below maximum coupling capacitances.
Geometry (design methodology) constraints are introduced to reduce the overall complexity of the design process. Examples include the use of preferred wiring directions during routing, and the placement of standard cells in rows.
Types of constraints

## Slide 18: 1.6 Algorithms and Complexity
Runtime complexity: the time required by the algorithm to complete as a function of some natural measure of the problem size, allows comparing the scalability of various algorithms
Complexity is represented in an asymptotic sense, with respect to the input size n, using big-Oh notation or O(…)
Runtime t(n) is order f (n), written as t(n) = O(f (n)) when
where k is a real number
Example: t(n) = 7n! + n2 + 100, then t(n) = O(n!) because n! is the fastest growing term as n  .
Runtime complexity

## Slide 19: 1.6 Algorithms and Complexity
Example: Exhaustively Enumerating All Placement Possibilities
  Given: n cells
  Task: find a single-row placement of n cells with minimum total wirelength by using exhaustive enumeration.
  Solution: The solution space consists of n! placement options. If generating and evaluating the wirelength of each possible placement solution takes 1 s and n = 20, the total time needed to find an optimal solution would be 77,147 years!
A number of physical design problems have best-known algorithm complexities that grow exponentially with n, e.g., O(n!), O(nn), and O(2n).
Many of these problems are NP-hard (NP: non-deterministic polynomial time)
  No known algorithms can ensure, in a time-efficient manner, globally optimal solution
Heuristic algorithms are used to find near-optimal solutions
Runtime complexity

## Slide 20: 1.6 Algorithms and Complexity
Deterministic: All decisions made by the algorithm are repeatable, i.e., not random. One example of a deterministic heuristic is Dijkstra’s shortest path algorithm.
Stochastic: Some decisions made by the algorithm are made randomly, e.g., using a pseudo-random number generator. Thus, two independent runs of the algorithm will produce two different solutions with high probability. One example of a stochastic algorithm is simulated annealing.
In terms of structure, a heuristic algorithm can be
  Constructive: The heuristic starts with an initial, incomplete (partial) solution and adds components until a complete solution is obtained.
  Iterative: The heuristic starts with a complete solution and repeatedly improves the current solution until a preset termination criterion is reached.
Heuristic algorithms

## Slide 21: 1.6 Algorithms and Complexity
Heuristic algorithms
Constructive Algorithm
Iterative Improvement
no
yes
Termination Criterion Met?
Return Best-Seen Solution
Problem Instance
Initial Solution

## Slide 22: 1.7 Graph Theory Terminology
Graph
Hypergraph
Multigraph
a
b
c
d
e
f
g
b
e
d
a
c
f
a
b
c
© 2022 Springer Verlag

## Slide 23: 1.7 Graph Theory Terminology
Directed graphs with cycles
Directed acyclic graph
c
a
b
d
e
f
g
a
b
c
a
b
d
e
f
g

## Slide 24: 1.7 Graph Theory Terminology
Undirected graph with maximum node degree 3
Directed tree
a
b
c
d
e
f
g
a
b
c
d
e
f
g
h
i
j
k

## Slide 25: 1.7 Graph Theory Terminology
Rectilinear minimum spanning tree (RMST)
Rectilinear Steiner minimum tree (RSMT)
b (2,6)
a (2,1)
c (6,4)
c (6,4)
Steiner point
b (2,6)
a (2,1)
© 2022 Springer Verlag

## Slide 26: 1.8 Common EDA Terminology
Netlist
a
b
x
y
z
c
N1
N2
N3
N4
(a: N1)
(b: N2)
(c: N5)
(x: IN1 N1, IN2 N2, OUT N3)
(y: IN1 N1, IN2 N2, OUT N4)
(z: IN1 N3, IN2 N4, OUT N5)
(N1: a, x.IN1, y.IN1)
(N2: b, x.IN2, y.IN2)
(N3: x.OUT, z.IN1)
(N4: y.OUT, z.IN2)
(N5: z.OUT, c)
Pin-Oriented Netlist
Net-Oriented Netlist
N5

## Slide 27: 1.8 Common EDA Terminology
Connectivity graph
a
b
x
y
z
c
N1
N2
N3
N4
N5
a
b
x
y
z
c

## Slide 28: 1.8 Common EDA Terminology
Connectivity matrix
a
b
x
y
z
c
N1
N2
N3
N4
N5
0
1
0
0
0
0
c
1
0
1
1
0
0
z
0
1
0
2
1
1
y
0
1
2
0
1
1
x
0
0
1
1
0
0
b
0
0
1
1
0
0
a
c
z
y
x
b
a

## Slide 29: 1.8 Common EDA Terminology
Distance metric between two points P1 (x1,y1) and P2 (x2,y2)
P1 (2,4)
P2 (6,1)
dM = 7
dM = 7
with n = 2: Euclidean distance
n = 1: Manhattan distance
dE = 5

## Slide 30: Summary of Chapter 1
IC production experienced huge growth since the 1960s
  Exponential decrease in transistor size, cost per transistor, power per transistor, etc
IC design is impossible without simplification and automation
  Row-based standard-cell layout with design rules
  Traditionally, each step in the VLSI design flow has been automated separately by software (CAD) tools
Software tools use sophisticated algorithms
  Many problems in physical design are NP-hard – solved by heuristic algorithms that find near-optimal solutions
  Deterministic versus stochastic algorithms
  Constructive algorithms versus iterative improvement
  Graph algorithms – deal with circuit connectivity
  Computational geometry – deal with circuit layout