## Slide 1
Chapter 2 – Netlist and System Partitioning

## Slide 2: Chapter 2 – Netlist and System Partitioning
2.1 Introduction
2.2 Terminology
2.3 Optimization Goals
2.4 Partitioning Algorithms
  2.4.1 Kernighan-Lin (KL) Algorithm
  2.4.2 Extensions of the Kernighan-Lin Algorithm
  2.4.3 Fiduccia-Mattheyses (FM) Algorithm
2.5 Framework for Multilevel Partitioning
  2.5.1 Clustering
  2.5.2 Multilevel Partitioning
2.6 System Partitioning onto Multiple FPGAs

## Slide 3: 2.1 Introduction
ENTITY test is port a: in bit; end ENTITY test;
DRC LVS
ERC
Circuit Design
Functional Design and Logic Design
Physical Design
Physical Verification and Signoff
Fabrication
System Specification
Architectural Design
Chip
Packaging and Testing
Chip Planning
Placement
Signal Routing
Partitioning
Timing Closure
Clock Tree Synthesis
© 2022 Springer Verlag

## Slide 4: 2.1 Introduction
Circuit:
Cut ca: four external connections
1
2
4
5
3
6
7
8
5
6
4
8
7
2
3
1
5
6
4
8
7
2
3
1
Cut ca
Cut cb
Block A
Block B
Block A
Block B
Cut cb: two external connections
© 2022 Springer Verlag

## Slide 5: 2.2 Terminology
5
6
4
2
1
3
3
2
4
5
6
1
Graph G2: Nodes 1, 2, 6.
Graph G1: Nodes 3, 4, 5.
Collection of cut edges Cut set: (1,3), (2,3), (5,6),
Block (Partition)
Cells

## Slide 6: 2.3 Optimization Goals
Given a graph G(V,E) with |V| nodes and |E| edges where each node v  V and each edge e  E.
Each node has area s(v) and each edge has cost or weight w(e).
The objective is to divide the graph G into k disjoint subgraphs such that all optimization goals are achieved and all original edge relations are respected.

## Slide 7: 2.3 Optimization Goals
In detail, what are the optimization goals?
  Number of connections between partitions is minimized
  Each partition meets all design constraints (size, number of external connections..)
  Balance every partition as well as possible
How can we meet these goals?
  Unfortunately, this problem is NP-hard
  Efficient heuristics are developed in the 1970s and 1980s. They are high quality and in low-order polynomial time.
7

## Slide 8: Chapter 2 – Netlist and System Partitioning
2.1 Introduction
2.2 Terminology
2.3 Optimization Goals
2.4 Partitioning Algorithms
  2.4.1 Kernighan-Lin (KL) Algorithm
  2.4.2 Extensions of the Kernighan-Lin Algorithm
  2.4.3 Fiduccia-Mattheyses (FM) Algorithm
2.5 Framework for Multilevel Partitioning
  2.5.1 Clustering
  2.5.2 Multilevel Partitioning
2.6 System Partitioning onto Multiple FPGAs

## Slide 9: 2.4.1 Kernighan-Lin (KL) Algorithm
Given: A graph with 2n nodes where each node has the same weight.
Goal: A partition (division) of the graph into two disjoint subsets A and B with minimum cut cost and |A| = |B| = n.
2
5
6
3
1
4
7
8
Example: n = 4
Block A
Block B

## Slide 10: 2.4.1 Kernighan-Lin (KL) Algorithm – Terminology
Cost D(v) of moving a node v
D(v) = |Ec(v)| – |Enc(v)| ,
where
Ec(v) is the set of v’s incident edges that are cut by the cut line, and
Enc(v) is the set of v’s incident edges that are not cut by the cut line.
High costs (D > 0) indicate that the node should move, while low costs (D < 0) indicate that the node should stay within the same partition.
2
5
6
3
1
4
7
8
Node 3:
D(3) = 3-1=2
Node 7:
D(7) = 2-1=1

## Slide 11: 2.4.1 Kernighan-Lin (KL) Algorithm – Terminology
Gain of swapping a pair of nodes a und b
g = D(a) + D(b) - 2* c(a,b),
where
D(a), D(b) are the respective costs of nodes a, b
c(a,b) is the connection weight between a and b:
If an edge exists between a and b, then c(a,b) = edge weight (here 1),
otherwise, c(a,b) = 0.
The gain g indicates how useful the swap between two nodes will be
The larger g, the more the total cut cost will be reduced
2
5
6
3
1
4
7
8

## Slide 12: 2.4.1 Kernighan-Lin (KL) Algorithm – Terminology
Gain of swapping a pair of nodes a und b
g = D(a) + D(b) - 2* c(a,b),
where
D(a), D(b) are the respective costs of nodes a, b
c(a,b) is the connection weight between a and b:
If an edge exists between a and b, then c(a,b) = edge weight (here 1),
otherwise, c(a,b) = 0.
2
5
6
3
1
4
7
8
Node 3:
D(3) = 3-1=2
Node 7:
D(7) = 2-1=1
g (3,7) = D(3) + D(7) - 2* c(a,b) = 2 + 1 – 2 = 1
=> Swapping nodes 3 and 7 would reduce the cut size by 1
2
5
6
3
1
4
7
8

## Slide 13: 2.4.1 Kernighan-Lin (KL) Algorithm – Terminology
Gain of swapping a pair of nodes a und b
g = D(a) + D(b) - 2* c(a,b),
where
D(a), D(b) are the respective costs of nodes a, b
c(a,b) is the connection weight between a and b:
If an edge exists between a and b, then c(a,b) = edge weight (here 1),
otherwise, c(a,b) = 0.
2
5
6
3
1
4
7
8
Node 3:
D(3) = 3-1=2
Node 5:
D(5) = 2-1=1
g (3,5) = D(3) + D(5) - 2* c(a,b) = 2 + 1 – 0 = 3
=> Swapping nodes 3 and 5 would reduce the cut size by 3
2
5
6
3
1
4
7
8

## Slide 14: 2.4.1 Kernighan-Lin (KL) Algorithm – Terminology
Gain of swapping a pair of nodes a und b
The goal is to find a pair of nodes a and b to exchange such that g is maximized and swap them.

## Slide 15: 2.4.1 Kernighan-Lin (KL) Algorithm – Terminology
Maximum positive gain Gm of a pass
The maximum positive gain Gm corresponds to the best prefix of m swaps within the swap sequence of a given pass.
These m swaps lead to the partition with the minimum cut cost encountered during the pass.
Gm is computed as the sum of Δg values over the first m swaps of the pass, with m chosen such that Gm is maximized.

## Slide 16: 2.4.1 Kernighan-Lin (KL) Algorithm – One pass

## Slide 17: 2.4.1 Kernighan-Lin (KL) Algorithm – Example
2
5
6
3
1
4
7
8
Cut cost: 9
Not fixed: 1,2,3,4,5,6,7,8

## Slide 18: 2.4.1 Kernighan-Lin (KL) Algorithm – Example
2
5
6
3
1
4
7
8
Cut cost: 9
Not fixed: 1,2,3,4,5,6,7,8
D(1) = 1 D(5) = 1 D(2) = 1 D(6) = 2 D(3) = 2 D(7) = 1 D(4) = 1 D(8) = 1
Costs D(v) of each node:
Nodes that lead to maximum gain

## Slide 19: 2.4.1 Kernighan-Lin (KL) Algorithm – Example
2
5
6
3
1
4
7
8
Cut cost: 9
Not fixed: 1,2,3,4,5,6,7,8
D(1) = 1 D(5) = 1 D(2) = 1 D(6) = 2 D(3) = 2 D(7) = 1 D(4) = 1 D(8) = 1 g1 = 2+1-0 = 3
Swap (3,5)
G1 = g1 =3
Nodes that lead to maximum gain
Gain in the current pass
Costs D(v) of each node:
Gain after node swapping

## Slide 20: 2.4.1 Kernighan-Lin (KL) Algorithm – Example
Cut cost: 9
Not fixed: 1,2,3,4,5,6,7,8
2
5
6
3
1
4
7
8
D(1) = 1 D(5) = 1 D(2) = 1 D(6) = 2 D(3) = 2 D(7) = 1 D(4) = 1 D(8) = 1 g1 = 2+1-0 = 3
Swap (3,5)
G1 = g1 =3
Nodes that lead to maximum gain
Gain in the current pass
Gain after node swapping
2
5
6
3
1
4
7
8

## Slide 21: 2.4.1 Kernighan-Lin (KL) Algorithm – Example
Cut cost: 9
Not fixed: 1,2,3,4,5,6,7,8
Cut cost: 6
Not fixed: 1,2,4,6,7,8
D(1) = 1 D(5) = 1 D(2) = 1 D(6) = 2 D(3) = 2 D(7) = 1 D(4) = 1 D(8) = 1 g1 = 2+1-0 = 3
Swap (3,5)
G1 = g1 =3
2
5
6
3
1
4
7
8
2
5
6
3
1
4
7
8

## Slide 22: 2.4.1 Kernighan-Lin (KL) Algorithm – Example
Cut cost: 9
Not fixed: 1,2,3,4,5,6,7,8
Cut cost: 6
Not fixed: 1,2,4,6,7,8
D(1) = 1 D(5) = 1 D(2) = 1 D(6) = 2 D(3) = 2 D(7) = 1 D(4) = 1 D(8) = 1 g1 = 2+1-0 = 3
Swap (3,5)
G1 = g1 =3
D(1) = -1 D(6) = 2 D(2) = -1 D(7)=-1 D(4) = 3 D(8)=-1
2
5
6
3
1
4
7
8
2
5
6
3
1
4
7
8

## Slide 23: 2.4.1 Kernighan-Lin (KL) Algorithm – Example
Cut cost: 9
Not fixed: 1,2,3,4,5,6,7,8
Cut cost: 6
Not fixed: 1,2,4,6,7,8
2
5
6
3
1
4
7
8
D(1) = 1 D(5) = 1 D(2) = 1 D(6) = 2 D(3) = 2 D(7) = 1 D(4) = 1 D(8) = 1 g1 = 2+1-0 = 3
Swap (3,5)
G1 = g1 =3
D(1) = -1 D(6) = 2 D(2) = -1 D(7)=-1 D(4) = 3 D(8)=-1 g2 = 3+2-0 = 5
Swap (4,6)
G2 = G1+g2 =8
Nodes that lead to maximum gain
Gain in the current pass
Gain after node swapping
2
5
6
3
1
4
7
8
2
5
6
3
1
4
7
8

## Slide 24: 2.4.1 Kernighan-Lin (KL) Algorithm – Example
Cut cost: 9
Not fixed: 1,2,3,4,5,6,7,8
Cut cost: 6
Not fixed: 1,2,4,6,7,8
Cut cost: 1
Not fixed: 1,2,7,8
2
5
6
3
1
4
7
8
Cut cost: 7
Not fixed: 2,8
D(1) = 1 D(5) = 1 D(2) = 1 D(6) = 2 D(3) = 2 D(7) = 1 D(4) = 1 D(8) = 1 g1 = 2+1-0 = 3
Swap (3,5)
G1 = g1 =3
D(1) = -1 D(6) = 2 D(2) = -1 D(7)=-1 D(4) = 3 D(8)=-1 g2 = 3+2-0 = 5
Swap (4,6)
G2 = G1+g2 =8
D(1) = -3 D(7)=-3 D(2) = -3 D(8)=-3 g3 = -3-3-0 = -6
Swap (1,7)
G3= G2 +g3 = 2
Gain in the current pass
Nodes that lead to maximum gain
Gain after node swapping
2
5
6
3
1
4
7
8
2
5
6
3
1
4
7
8
2
5
6
3
1
4
7
8

## Slide 25: 2.4.1 Kernighan-Lin (KL) Algorithm – Example
Cut cost: 9
Not fixed: 1,2,3,4,5,6,7,8
2
5
6
3
1
4
7
8
Cut cost: 9
Not fixed: –
Cut cost: 6
Not fixed: 1,2,4,6,7,8
Cut cost: 1
Not fixed: 1,2,7,8
Cut cost: 7
Not fixed: 2,8
D(1) = 1 D(5) = 1 D(2) = 1 D(6) = 2 D(3) = 2 D(7) = 1 D(4) = 1 D(8) = 1 g1 = 2+1-0 = 3
Swap (3,5)
G1 = g1 =3
D(1) = -1 D(6) = 2 D(2) = -1 D(7)=-1 D(4) = 3 D(8)=-1 g2 = 3+2-0 = 5
Swap (4,6)
G2 = G1+g2 =8
D(1) = -3 D(7)=-3 D(2) = -3 D(8)=-3 g3 = -3-3-0 = -6
Swap (1,7)
G3= G2 +g3 = 2
D(2) = -1 D(8)=-1
g4 = -1-1-0 = -2
Swap (2,8)
G4 = G3 +g4 = 0
2
5
6
3
1
4
7
8
2
5
6
3
1
4
7
8
2
5
6
3
1
4
7
8
2
5
6
3
1
4
7
8
© 2022 Springer Verlag

## Slide 26: 2.4.1 Kernighan-Lin (KL) Algorithm – Example
Maximum positive gain Gm = 8 with m = 2.
D(1) = 1 D(5) = 1 D(2) = 1 D(6) = 2 D(3) = 2 D(7) = 1 D(4) = 1 D(8) = 1 g1 = 2+1-0 = 3
Swap (3,5)
G1 = g1 =3
D(1) = -1 D(6) = 2 D(2) = -1 D(7)=-1 D(4) = 3 D(8)=-1 g2 = 3+2-0 = 5
Swap (4,6)
G2 = G1+g2 =8
D(1) = -3 D(7)=-3 D(2) = -3 D(8)=-3 g3 = -3-3-0 = -6
Swap (1,7)
G3= G2 +g3 = 2
D(2) = -1 D(8)=-1
g4 = -1-1-0 = -2
Swap (2,8)
G4 = G3 +g4 = 0

## Slide 27: 2.4.1 Kernighan-Lin (KL) Algorithm – Example
D(1) = 1 D(5) = 1 D(2) = 1 D(6) = 2 D(3) = 2 D(7) = 1 D(4) = 1 D(8) = 1 g1 = 2+1-0 = 3
Swap (3,5)
G1 = g1 =3
D(1) = -1 D(6) = 2 D(2) = -1 D(7)=-1 D(4) = 3 D(8)=-1 g2 = 3+2-0 = 5
Swap (4,6)
G2 = G1+g2 =8
D(1) = -3 D(7)=-3 D(2) = -3 D(8)=-3 g3 = -3-3-0 = -6
Swap (1,7)
G3= G2 +g3 = 2
D(2) = -1 D(8)=-1
g4 = -1-1-0 = -2
Swap (2,8)
G4 = G3 +g4 = 0
Since Gm > 0, the first m = 2 swaps (3,5) and (4,6) are executed.
2
5
6
3
1
4
7
8
Since Gm > 0, more passes are needed until Gm  0.
Maximum positive gain Gm = 8 with m = 2.

## Slide 28: 2.4.1 Kernighan-Lin (KL) Algorithm – Example
D(1) = 1 D(5) = 1 D(2) = 1 D(6) = 2 D(3) = 2 D(7) = 1 D(4) = 1 D(8) = 1 g1 = 2+1-0 = 3
Swap (3,5)
G1 = g1 =3
D(1) = -1 D(6) = 2 D(2) = -1 D(7)=-1 D(4) = 3 D(8)=-1 g2 = 3+2-0 = 5
Swap (4,6)
G2 = G1+g2 =8
D(1) = -3 D(7)=-3 D(2) = -3 D(8)=-3 g3 = -3-3-0 = -6
Swap (1,7)
G3= G2 +g3 = 2
D(2) = -1 D(8)=-1
g4 = -1-1-0 = -2
Swap (2,8)
G4 = G3 +g4 = 0
Since Gm > 0, the first m = 2 swaps (3,5) and (4,6) are executed.
2
5
6
3
1
4
7
8
Since Gm > 0, more passes are needed until Gm  0.
Maximum positive gain Gm = 8 with m = 2.

## Slide 29: 2.4.1 Kernighan-Lin (KL) Algorithm – Example
In the Kernighan-Lin (KL) algorithm, the concept of "maximum positive gain Gm​" is a key part of the iterative improvement process during each pass. Let me explain this in detail, building on your understanding.
What is Gm​?
•In each pass of the KL algorithm, we generate a sequence of potential node swaps (each swap involves one node from partition A and one from partition B). For each swap in the sequence, we compute a gain value Δg(which measures how much the cut size would change if that swap were performed).
•The cumulative gain Gk​after the first kswaps is defined as the sum of the Δgvalues for those swaps: Gk​=∑i=1k​Δgi​.
•The ​​maximum positive gain Gm​​​ is the largest positive value of Gk ​for any k in the sequence. That is, we find the value of m such that Gm​is maximized (and positive). This represents the best cumulative improvement achievable by performing the first m swaps in the sequence.
Summarize of KL Algorithm

## Slide 30: 2.4.1 Kernighan-Lin (KL) Algorithm – Example
Why is Gm ​important?
•Gm​ corresponds to the point in the swap sequence where the cut cost is minimized during the pass. Even if some individual swaps have negative gains, the cumulative effect of the first m swaps might still be positive overall, leading to a better partition.
•The algorithm then actually performs these m swaps (i.e., physically moves the nodes) to update the partitions. This ensures that we only commit to swaps that collectively reduce the cut size.
•If no positive Gm ​exists (i.e., all cumulative gains are non-positive), the algorithm stops because no further improvement is possible.
Summarize of KL Algorithm

## Slide 31: 2.4.1 Kernighan-Lin (KL) Algorithm – Example
How is Gm computed in practice?
During a pass:
1. Initialize​​: Start with an initial partition (A, B).
2. Compute gains​​: For all unlocked nodes, compute the gain Δg for each possible swap pair. Select the pair with the highest Δg, lock those nodes, and record Δg1. Update the gains of affected nodes due to the virtual swap.
3.​​ Repeat​​: Continue selecting the best swap pair from the remaining unlocked nodes, recording Δg2,Δg3,…until all nodes are locked. This forms a sequence of gains Δg1,Δg2,…, Δgn/2 (where n is the number of nodes).
4. Compute cumulative gains​​: Calculate for k=1,2,…,n/2.
5. Find Gm​​​: Find the value mthat maximizes Gk​. If Gm​>0, perform the first mswaps; otherwise, do nothing.
Summarize of KL Algorithm

## Slide 32: 2.4.1 Kernighan-Lin (KL) Algorithm – Example
Example
Suppose in a pass, we have a sequence of gains: Δg1​=3,Δg2​=−1,Δg3​=2,Δg4​=−2.

## Slide 33: 2.4.1 Kernighan-Lin (KL) Algorithm – Example
Example
Suppose in a pass, we have a sequence of gains: Δg1​=3,Δg2​=−1,Δg3​=2,Δg4​=−2.
•Cumulative gains:
•G1​=3
•G2​=3+(−1)=2
•G3​=2+2=4
•G4​=4+(−2)=2
•Here, Gm​=4at m=3, which is the maximum positive cumulative gain. So, we would perform the first 3 swaps, even though the second swap had a negative gain, because the overall effect is positive.

## Slide 34: 2.4.1 Kernighan-Lin (KL) Algorithm – Example
Question 1
Think about the following question: Suppose in a pass, we have a sequence of gains: Δg1 =3,Δg2=−1,Δg3=2,Δg4=−2, could we only choose Δg1 and Δg2 as the exchange?
Question 2
what is the advantage of KL algorithm?
Question 3
Is the KL algorithm the global optimum in graph parition?

## Slide 35: 2.4.2 Extensions of the Kernighan-Lin (KL) Algorithm
Unequal partition sizes
  Apply the KL algorithm with only min(|A|,|B|) pairs swapped
Unequal node weights
  Try to rescale weights to integers, e.g., as multiples of the greatest common divisor of all node weights
  Maintain area balance or allow a one-move deviation from balance
k-way partitioning (generating k partitions)
  Apply the KL two-way partitioning algorithm to all possible pairs of partitions
  Recursive partitioning (convenient when k is a power of two)
  Direct k-way extensions exist
35

## Slide 36: 2.4.3 Fiduccia-Mattheyses (FM) Algorithm
Single cells are moved independently instead of swapping pairs of cells --- cannot and do not need to maintain exact partition balance
  The area of each individual cell is taken into account
  Applicable to partitions of unequal size and in the presence of initially fixed cells
Cut costs are extended to include hypergraphs
  nets with 2+ pins
While the KL algorithm aims to minimize cut costs based on edges, the FM algorithm minimizes cut costs based on nets
Nodes and subgraphs are referred to as cells and blocks, respectively

## Slide 37: 2.4.3 Fiduccia-Mattheyses (FM) Algorithm
Given: a hypergraph G(V,H) with nodes and weighted hyperedges partition size constraints
Goal: to assign all nodes to disjoint partitions, so as to minimize the total cost (weight) of all cut nets while satisfying partition size constraints

## Slide 38: 2.4.3 Fiduccia-Mattheyses (FM) Algorithm – Terminology
Gain g(c) for cell c
g(c) = FS(c) – TE(c) ,
where
the “moving force“ FS(c) is the number of nets connected to c but not connected to any other cells within c’s partition, i.e., cut nets that connect only to c, and
the “retention force“ TE(c) is the number of uncut nets connected to c.
The higher the gain g(c), the higher is the priority to move the cell c to the other partition.
Cell 2: FS(2) = 0 TE(2) = 1 g(2) = -1
1
3
4
2
5
a
b
c
d
e

## Slide 39: 2.4.3 Fiduccia-Mattheyses (FM) Algorithm – Terminology
Gain g(c) for cell c
g(c) = FS(c) – TE(c) ,
where
the “moving force“ FS(c) is the number of nets connected to c but not connected to any other cells within c’s partition, i.e., cut nets that connect only to c, and
the “retention force“ TE(c) is the number of uncut nets connected to c.
Cell 1: FS(1) = 2 TE(1) = 1 g(1) = 1
Cell 2: FS(2) = 0 TE(2) = 1 g(2) = -1
Cell 3: FS(3) = 1 TE(3) = 1 g(3) = 0
Cell 4: FS(4) = 1 TE(4) = 1 g(4) = 0
Cell 5: FS(5) = 1 TE(5) = 0 g(5) = 1
1
3
4
2
5
a
b
c
d
e
1
3
4
2
5
a
b
c
d
e

## Slide 40: 2.4.3 Fiduccia-Mattheyses (FM) Algorithm – Terminology
Maximum positive gain Gm of a pass
The maximum positive gain Gm is the cumulative cell gain of m moves that produce a minimum cut cost.
Gm is determined by the maximum sum of cell gains g over a prefix of m moves in a pass

## Slide 41: 2.4.3 Fiduccia-Mattheyses (FM) Algorithm – Terminology
Ratio factor
The ratio factor is the relative balance between the two partitions with respect to cell area
It is used to prevent all cells from clustering into one partition.
The ratio factor r is defined as
where area(A) and area(B) are the total respective areas of partitions A and B

## Slide 42: 2.4.3 Fiduccia-Mattheyses (FM) Algorithm – Terminology
Balance criterion
The balance criterion enforces the ratio factor.
To ensure feasibility, the maximum cell area areamax(V) must be taken into account.
A partitioning of V into two partitions A and B is said to be balanced if
[ r ∙ area(V) – areamax(V) ] ≤ area(A) ≤ [ r ∙ area(V) + areamax(V) ]

## Slide 43: 2.4.3 Fiduccia-Mattheyses (FM) Algorithm – Terminology
Base cell
A base cell is a cell c that has the greatest cell gain g(c) among all free cells, and whose move does not violate the balance criterion.
Cell 1: FS(1) = 2 TE(1) = 1 g(1) = 1
Cell 2: FS(2) = 0 TE(2) = 1 g(2) = -1
Cell 3: FS(3) = 1 TE(3) = 1 g(3) = 0
Cell 4: FS(4) = 1 TE(4) = 1 g(4) = 0
Base cell

## Slide 44: 2.4.3 Fiduccia-Mattheyses (FM) Algorithm - One pass

## Slide 45: 2.4.3 Fiduccia-Mattheyses (FM) Algorithm – Example
1
3
4
2
5
A
B
a
b
c
d
e
Step 0: Compute the balance criterion
[ r ∙ area(V) – areamax(V) ] ≤ area(A) ≤ [ r ∙ area(V) + areamax(V) ]
0,375 * 16 – 5 = 1  area(A)  11 = 0,375 * 16 +5.
Given: Ratio factor r = 0,375
area(Cell_1) = 2 area(Cell_2) = 4 area(Cell_3) = 1 area(Cell_4) = 4 area(Cell_5) = 5.

## Slide 46: 2.4.3 Fiduccia-Mattheyses (FM) Algorithm – Example
1
3
4
2
5
A
B
a
b
c
d
e
Step 1: Compute the gains of each cell
Cell 1: FS(Cell_1) = 2 TE(Cell_1) = 1 g(Cell_1) = 1
Cell 2: FS(Cell_2) = 0 TE(Cell_2) = 1 g(Cell_2) = -1
Cell 3: FS(Cell_3) = 1 TE(Cell_3) = 1 g(Cell_3) = 0
Cell 4: FS(Cell_4) = 1 TE(Cell_4) = 1 g(Cell_4) = 0
Cell 5: FS(Cell_5) = 1 TE(Cell_5) = 0 g(Cell_5) = 1

## Slide 47: 2.4.3 Fiduccia-Mattheyses (FM) Algorithm – Example
1
3
4
2
5
A
B
a
b
c
d
e
Cell1: FS(Cell_1) = 2 TE(Cell_1) = 1 g(Cell_1) = 1
Cell 2: FS(Cell_2) = 0 TE(Cell_2) = 1 g(Cell_2) = -1
Cell 3: FS(Cell_3) = 1 TE(Cell_3) = 1 g(Cell_3) = 0
Cell 4: FS(Cell_4) = 1 TE(Cell_4) = 1 g(Cell_4) = 0
Cell 5: FS(Cell_5) = 1 TE(Cell_5) = 0 g(Cell_5) = 1
Step 2: Select the base cell
Possible base cells are Cell 1 and Cell 5
Balance criterion after moving Cell 1: area(A) = area(Cell_2) = 4
Balance criterion after moving Cell 5: area(A) = area(Cell_1) + area(Cell_2) + area(Cell_5) = 11
Both moves respect the balance criterion, but Cell 1 is selected, moved,
and fixed as a result of the tie-breaking criterion.

## Slide 48: 2.4.3 Fiduccia-Mattheyses (FM) Algorithm – Example
1
3
4
2
5
A
B
a
b
c
d
e
Step 3: Fix base cell, update g values
Cell 2: FS(Cell_2) = 2 TE(Cell_2) = 0 g(Cell_2) = 2
Cell 3: FS(Cell_3) = 0 TE(Cell_3) = 1 g(Cell_3) = -1
Cell 4: FS(Cell_4) = 0 TE(Cell_4) = 2 g(Cell_4) = -2
Cell 5: FS(Cell_5) = 0 TE(Cell_5) = 1 g(Cell_5) = -1
After Iteration i = 1: Partition A1 = 2, Partition B1 = 1,3,4,5, with fixed cell 1.

## Slide 49: 2.4.3 Fiduccia-Mattheyses (FM) Algorithm – Example
1
3
4
2
5
A
B
a
b
c
d
e
Cell 2: FS(Cell_2) = 2 TE(Cell_2) = 0 g(Cell_2) = 2
Cell 3: FS(Cell_3) = 0 TE(Cell_3) = 1 g(Cell_3) = -1
Cell 4: FS(Cell_4) = 0 TE(Cell_4) = 2 g(Cell_4) = -2
Cell 5: FS(Cell_5) = 0 TE(Cell_5) = 1 g(Cell_5) = -1
Iteration i = 2
Cell 2 has maximum gain g2 = 2, area(A) = 0, balance criterion is violated.
Cell 3 has next maximum gain g2 = -1, area(A) = 5, balance criterion is met.
Cell 5 has next maximum gain g2= -1, area(A) = 9, balance criterion is met.
Move cell 3, updated partitions: A2 = {2,3}, B2 = {1,4,5}, with fixed cells {1,3}
Iteration i = 1

## Slide 50: 2.4.3 Fiduccia-Mattheyses (FM) Algorithm – Example
Cell 2: g(Cell_2) = 1
Cell 4: g(Cell_4) = 0
Cell 5: g(Cell_5) = -1
Iteration i = 3
Cell 2 has maximum gain g3 = 1, area(A) = 1, balance criterion is met. Move cell 2, updated partitions: A3 = {3}, B3 = {1,2,4,5}, with fixed cells {1,2,3}
1
3
4
2
5
A
B
a
b
c
d
e
Iteration i = 2

## Slide 51: 2.4.3 Fiduccia-Mattheyses (FM) Algorithm – Example
Cell 4: g(Cell_4) = 0
Cell 5: g(Cell_5) = -1
Iteration i = 4
Cell 4 has maximum gain g4 = 0, area(A) = 5, balance criterion is met. Move cell 4, updated partitions: A4 = {3,4}, B3 = {1,2,5}, with fixed cells {1,2,3,4}
1
3
4
2
5
B
A
a
b
c
d
e
Iteration i = 3

## Slide 52: 2.4.3 Fiduccia-Mattheyses (FM) Algorithm – Example
Cell 5: g(Cell_5) = -1
Iteration i = 5
Cell 5 has maximum gain g5 = -1, area(A) = 10, balance criterion is met. Move cell 5, updated partitions: A4 = {3,4,5}, B3 = {1,2}, all cells {1,2,3,4,5} fixed.
1
3
4
2
5
B
A
a
b
c
d
e
Iteration i = 4

## Slide 53: 2.4.3 Fiduccia-Mattheyses (FM) Algorithm – Example
Step 5: Find best move sequence c1 … cm
G1 = g1 = 1 G2 = g1 + g2 = 0 G3 = g1 + g2 + g3 = 1 G4 = g1 + g2 + g3 + g4 = 1 G5 = g1 + g2 + g3 + g4 + g5 = 0.
Maximum positive cumulative gain
found in iterations 1, 3 and 4.
The move prefix m = 4 is selected due to the better balance ratio (area(A) = 5); the four cells 1, 2, 3 and 4 are then moved.
Result of Pass 1: Current partitions: A = {3,4}, B = {1,2,5}, cut cost reduced from 3 to 2.
1
3
4
2
5
B
A
a
b
c
d
e

## Slide 54: Runtime difference between KL & FM
Runtime of partitioning algorithms
  KL is sensitive to the number of nodes and edges
  FM is sensitive to the number of nodes and nets (hyperedges)
Asymptotic complexity of partitioning algorithms
  KL has cubic time complexity per pass
  FM has linear time complexity per pass
54

## Slide 55: Runtime difference between KL & FM
​​ Advantages:​​
High efficiency:​​ Time complexity is O(P), where P is the total number of pins in the hypergraph.
​​High-quality solutions:​​ Often finds near-optimal partitions.
​​Balance constraints:​​ Capable of handling partition size limitations.
​​Flexibility:​​ Applicable to various hypergraph structures.
​​ Disadvantages:​​
​​Local optima:​​ May get trapped in local optimal solutions.
Dependency on initial solution:​​ The quality of the solution is influenced by the initial partition.
Parameter sensitivity:​​ Performance is affected by the balance factor ε.
55

## Slide 56: Runtime difference between KL & FM
​​ FM and KL algorithm comparison
1. ​​Movement Strategy​​
​​KL​​: Requires finding and swapping vertex pairs (both from different partitions)
​​FM​​: Moves single vertices across partitions, which is more flexible and efficient
2. ​​Time Complexity​​
​​KL​​: O(n³) - Becomes impractical for large graphs
​​FM​​: O(P) - Linear in the number of pins, making it suitable for large hypergraphs
3. ​​Data Structures​​
​​KL​​: Uses simple lists to track vertices and gains
​​FM​​: Employs sophisticated gain buckets that allow O(1) access to the highest-gain vertex
4. ​​Balance Maintenance​​
​​KL​​: Often requires separate balancing steps after optimization
​​FM​​: Maintains balance constraints throughout the optimization process
56

## Slide 57: Runtime difference between KL & FM
​​ FM and KL algorithm comparison
5. ​​Application Scope​​
KL​​: Primarily designed for regular graphs
​​FM​​: Specifically designed for hypergraphs (common in VLSI design)
6. ​​Implementation Complexity​​
​​KL​​: More complex to implement due to pair selection logic
​​FM​​: Relatively simpler implementation with gain buckets
7. ​​Solution Quality​​
​​KL​​: Can find good solutions but may be slower
​​FM​​: Typically finds high-quality solutions more efficiently
8. ​​Practical Usage​​
​​KL​​: Foundational algorithm but less used in modern applications
​​FM​​: Widely used in VLSI design tools and other practical applications
57

## Slide 58: Runtime difference between KL & FM
​​ FM and KL algorithm comparison
Conclusion
The FM algorithm represents a significant improvement over the KL algorithm by:
Using single vertex moves instead of pairs
Employing efficient gain bucket data structures
Achieving linear time complexity
Better handling hypergraph structures
Maintaining balance constraints during optimization
While KL remains an important historical algorithm, FM is generally preferred for practical applications, particularly in VLSI design and large-scale hypergraph partitioning problems where efficiency and scalability are crucial.
58

## Slide 59: Runtime difference between KL & FM
​​ FM and KL algorithm comparison
Question
Why the algorithm complexity of KL is O(n³) and the FM is O(p)
59

## Slide 60: Runtime difference between KL & FM
​​ FM and KL algorithm comparison
Question
Why the algorithm complexity of KL is O(n³) and the FM is O(p)
60
1. Kernighan-Lin (KL) 算法为什么是 O(n³)
KL算法的核心操作是​​交换一对顶点​​（一个来自分区A，一个来自分区B）。它的复杂度主要来自以下几个步骤：
​​a) 初始化：​​ 计算所有顶点的增益。这需要遍历每个顶点，并查看其所有边。对于稀疏图，这大约是 O(n * 平均度数) ≈ O(n²)。
​​b) 主循环（这是复杂度的主要来源）：​​
KL算法的一个“通行”（pass）会进行大约 n/2 次交换。在每一次交换中，它需要：
1）寻找最佳顶点对：​​ 为了找到增益最高的那一对顶点，算法需要检查所有​​可能的候选对​​。在最坏情况下，这需要检查 |A| * |B| 对顶点。在算法开始时，|A| ≈ |B| ≈ n/2，所以这一步的复杂度是 O((n/2) * (n/2)) = ​​O(n²)​​。
2）交换并锁定顶点：​​ 交换选中的顶点对，并将它们锁定（在本轮后续过程中不再考虑）。

## Slide 61: Runtime difference between KL & FM
​​ FM and KL algorithm comparison
Question
Why the algorithm complexity of KL is O(n³) and the FM is O(p)
61
3） 更新增益：​​ 这对顶点的移动会影响它们邻居的增益。因此需要更新所有与这两个顶点相连的顶点的增益。对于稀疏图，每个顶点的邻居数量是常数，所以这步大约是 O(1)，但严格来说是 O(平均度数)。
​​复杂度计算：​​
主循环有 n/2 次迭代（每次交换一对顶点）。
在每次迭代中，​​寻找最佳顶点对​​的操作就需要 O(n²) 时间。
因此，一个完整通行（pass）的总时间复杂度是：​​(n/2) * O(n²) = O(n³)​​。
​​核心问题：​​ KL算法在每一轮迭代中，为了找一对最好的顶点，都需要进行一次全局搜索，扫描所有可能的配对。这个全局搜索的代价非常高。

## Slide 62: Runtime difference between KL & FM
​​ FM and KL algorithm comparison
Question
Why the algorithm complexity of KL is O(n³) and the FM is O(p)
62
Fiduccia-Mattheyses (FM) 算法为什么是 O(P)
FM算法是KL算法的改进版，它的核心操作是​​移动单个顶点​​（而不是交换一对）。它通过一个名为 ​​“增益桶”（Gain Bucket）​​ 的数据结构彻底解决了KL算法的性能瓶颈。
​​a) 关键改进1：单顶点移动​​
移动一个顶点比交换一对顶点更灵活，决策空间更大。
平衡约束通过限制分区大小来维护，而不是必须成对交换。
​​b) 关键改进2：增益桶数据结构（核心！）​​
这是FM算法效率飞跃的根本原因。增益桶是一个将增益值作为索引的数组（或字典），每个桶里存放所有具有该增益值的顶点。
​​初始化：​​ 算法开始时，计算所有顶点的增益，并将它们放入对应的增益桶中。​​这是一个O(P)的操作​​，因为需要计算每个顶点的增益，而计算一个顶点的增益需要查看其所有连接的边（即“引脚”）。P= 超图中所有超边的“引脚”数量之和。对于普通图，P就是边数乘以2（因为每条边有两个连接）
​​寻找最佳移动顶点：​​ 在KL中，这一步需要O(n²)。而在FM中，由于增益桶的存在，​​这一步是O(1)​​！你只需要直接查看最高增益对应的那个桶，并从里面取一个顶点即可。

## Slide 63: Runtime difference between KL & FM
​​ FM and KL algorithm comparison
Question
Why the algorithm complexity of KL is O(n³) and the FM is O(p)
63
Fiduccia-Mattheyses (FM) 算法为什么是 O(P)
移动顶点和更新增益：​​ 移动一个顶点v后，所有与v相连的顶点的增益都会改变。
在KL中，更新增益需要全局扫描。在FM中，更新操作非常高效：
1.将受影响的顶点从它们当前所在的增益桶中移除。
2.计算它们新的增益值。
3.将它们插入到新的增益值对应的桶中。
每个受影响的顶点的更新操作是​​常数时间O(1)​​。
一个顶点v的移动，会影响所有与它共享超边的顶点。这些顶点数量的总和，正好就是顶点v的​​引脚数​​。
​​c) 复杂度计算：​​
算法的一个通行（pass）会移动最多n个顶点。
处理整个通行所需的总工作量，是​​所有被移动顶点的影响代价之和​​。
移动一个顶点v的代价 ≈ 它的引脚数。
因此，一个通行处理所有顶点的总代价 ≈ ​​所有顶点的引脚数之和 = P​​。
所以，总时间复杂度为 ​​O(P)​​。

## Slide 64: Chapter 2 – Netlist and System Partitioning
2.1 Introduction
2.2 Terminology
2.3 Optimization Goals
2.4 Partitioning Algorithms
  2.4.1 Kernighan-Lin (KL) Algorithm
  2.4.2 Extensions of the Kernighan-Lin Algorithm
  2.4.3 Fiduccia-Mattheyses (FM) Algorithm
2.5 Framework for Multilevel Partitioning
  2.5.1 Clustering
  2.5.2 Multilevel Partitioning
2.6 System Partitioning onto Multiple FPGAs

## Slide 65: 2.5.1 Clustering
65
To simplify the problem, groups of tightly-connected nodes can be clustered, absorbing connections between these nodes
Size of each cluster is often limited so as to prevent degenerate clustering, i.e. a single large cluster dominates other clusters
Refinement should satisfy balance criteria

## Slide 66: 2.5.1 Clustering
a
b
c
d
e
a,b,c
d
e
a
b
d
c,e
Initital graph
Possible clustering hierarchies of the graph

## Slide 67: 2.5.2 Multilevel Partitioning
© 2022 Springer Verlag

## Slide 68: 2.6 System Partitioning onto Multiple FPGAs
FPGA
FPGA
FPGA
FPGA
FPIC
FPIC
FPIC
FPIC
FPGA
FPGA
RAM
Logic
Logic
Reconfigurable system with multiple FPGA and FPIC devices
Mapping of a typical system architecture onto multiple FPGAs

## Slide 69: Summary of Chapter 2
Circuit netlists can be represented by graphs
Partitioning a graph means assigning nodes to disjoint partitions
  Total size of each partition (number/area of nodes) is limited
  Objective: minimize the number connections between partitions
Basic partitioning algorithms
  Move-based, move are organized into passes
  KL swaps pairs of nodes from different partitions
  FM re-assigns one node at a time
  FM is faster, usually more successful
Multilevel partitioning
  Clustering
  FM partitioning
  Refinement (also uses FM partitioning)
Application: system partitioning into FPGAs
  Each FPGA is represented by a partition